## Slide 1: Introduction to Engineering Design II

## Slide 2: Goals
See an example of complex system design, using satellites

## Slide 3: What are Satellites?
Satellites are man-made objects in space that we use for many different things!
Television, internet, phones
Astronomy, research
Earth observing

## Slide 4: What are the physics behind satellites?
Is there gravity in space?
Do satellites have rockets on them?
How do satellites stay in orbit

## Slide 5: What is orbit?
Orbit is when a satellite circles the Earth
Satellites “stay” in orbit due to gravity
Gravity acts as a centripetal force
Let’s derive how orbits work!

## Slide 6: Derive

## Slide 7: How fast do satellites need to go to stay in orbit?
G = 6.67408 × 10-11 m3 kg-1 s-2
ME = 5.972 × 10^24 kg
r = rE + rO = 6,371 km + 429 km = 6,800 km
What is v?

## Slide 8: How fast do our satellites need to go?
At a height of 429 km above the Earth, our satellites need to go ~27,550 km/hr!
What happens to that speed if we increase the mass of the satellite?
What happens to that speed if we increase the height of the orbit? What about decrease?

## Slide 9: 1. Problem Statement: Designing a satellite
I want to create a system that can take pictures of Kazakhstan from space

## Slide 10: 2. Define System Objectives

## Slide 11: 2. Define System Objectives
Take a picture of all of Kazakhstan from space everyday for a year and send them back to Earth so we can look at them!

## Slide 12: 3. Define System Requirements

## Slide 13: 3. Define System Requirements
The system shall orbit the Earth at a height of at least 500km
The system shall take pictures of Kazakhstan at least once a day
The system shall remain in space for at least one year
The system shall be able to send its pictures back to Earth every day

## Slide 14: 4. Define Subsystem Objectives
Satellite

## Slide 15: 4. Define Subsystem Objectives
Satellite
Camera
Power
Communications
Orbit

## Slide 16: 5. Define Subsystem Requirements
1 Orbit
Camera
3 Communications
4 Power

## Slide 17: 5. Define Subsystem Requirements
1 Orbit
500 km orbit
orbit lasts for 1 year
orbit goes over Kazakhstan every day
Camera
Picture everyday
Camera lasts 1 year
Camera can see all of Kazakhstan
Camera can turn towards Kazakhstan
3 Communications
Send picture back to Earth every day
4 Power
Satellite can power itself
Power on communications and Camera

## Slide 18: 6. Repeat and Refine